## Slide 1: ceramics
Year 9 Visual Arts

## Slide 2: Glossary of Terms
Glossary term | Definition/Description
Handbuilding | This term refers to the one of several techniques of building pots using the only the hands and simple tools rather than the potter’s wheel.
Coil | This is the technique of building ceramic forms by rolling out coils, or ropes, of clay and joining them together with the fingers or a tool.
Molding | In this technique, clay is pressed into molds in order to create various shapes or forms.
Slip | Slip is liquid clay, with the consistency of cream
Firing | This is the process of heating the pottery to a specific temperature in order to bring about a particular change in the clay or the surface.
Bisque | The term bisque refers to ceramic ware that has been fired once without glaze.
Greenware | This refers to ceramic ware that has not been fired.

## Slide 3: Research Questions:
Where does clay come from?
How was it collected?
How was it used traditionally in different cultures?
Include examples(images)
What were the roles of potters and sculptors, past and present?

## Slide 4: Techniques of Ceramics:
Hand building techniques such as:
coil construction
slab construction
drape moulds
press moulds

## Slide 5: Ten Golden Rules for Ceramics
Clay must be thoroughly covered up with a plastic bag to keep it from drying out. This applies to works in progress and moist clay.
Clay dust can be harmful if you are exposed to it for long periods of time, so keep your area clean, clay scraps off the floor and clean with water and a sponge.
Clay can be no thicker than your thumb.
In order for clay to stick together it MUST be scored and slipped together while the clay is moist or leather hard.
Wedge clay to remove air bubbles, achieve uniform consistency, and to line up the particles of clay.
Trapped air can cause clay to explode. So hollow out sculptural forms and put needle holes from the bottom so air can escape.
Don't glaze the bottom of a piece.
Always wash the piece before glazing.
Always handle your project with two hands at all times. In other words BE CAREFUL it’s your hard work. Never lift pots by the rim.
NEVER HANDLE ANOTHER PERSONS WORK EVEN IF IT LOOKS COOL

## Slide 6: ASSESSMENT:
Design and create a functional artwork based on one of your learned skills which will be extended to incorporate a highly decorative element.
Carved out slab constructed pot
Slab constructed box with decorative lid or corners
Creature pots/planters
Egyptian style objects such as canopic jars
Animal or decorative bookends
Decorative moulded pots

## Slide 7: Contemporary Ceramic artists
Brigiat Maltese
Merran Esson
Irene Mbitjana Entata
Victor Spinski
Carol Long
Margaret Dodd.

## Slide 8: Research task
Students to design and research a PPT on one of the contemporary artists, using textbooks, and internet to research the artist.
Artists Background
Artists influences, nature, family, other contemporaries
What Pottery/ceramics technique did they use?
Examples of the artist’s work